## Slide 1: Communication and Computer Network CNS3200
Notes: 1

## Slide 2: Learning outcome
Identify components in data communication (C4)
Topics
  Introduction
  Data communication
  Components
  Example of Protocol
  Data Representation
  Transmission Mode
  Network

## Slide 3: Introduction
Why Data Communications?
accessibility – to get accurate information.
data/information sharing?
Eg: From one pc – data copied onto a floppy disk and physically reloaded to another pc/remote computer – time consuming, inconveniences.
Revolution is occurred in telecommunications networks
Technological advances drive communication links to carry more and faster signals.
3

## Slide 4: Data Communication
Definition:
  Telecommunication= means communication at a distance (tele is Greek for far). E.g: telephony, telegraphy, and television.
  Data =
    Facts, concepts, and instructions presented in whatever form is agreed upon by the parties creating and using data.
    In the context of computer IS, data are represented by binary information units (or bits) produced and consumed in the form of 0s and 1s.
Data communication
The exchange of data between two devices via some form of transmission medium (such as wire cable)
4

## Slide 5: Data Communication
The effectiveness of a data communication system depends on 4
fundamental characteristics :
  Delivery
The system must deliver data to the correct destination.
  Accuracy
  The system must deliver data accurately.
  Timeliness
  The system must deliver data in timely manner.
  Jitter
  Variation in arrival time.
5

## Slide 6: Data Communication
Data communication components
6

## Slide 7: Data Communication Components
A data communication system consists of 5 components :
  Message– The message is the information (data) to be communicated. Can consists of text, numbers, picture, audio, video.
  Sender – the device that sends the data message. Can be a computer, workstation, mobile phone, video cam etc
  Receiver – the device that receives the message. Can be a computer, workstation, mobile phone, tv etc.
  Medium – the physical path by which a message travels from sender to receiver. UTP cable, coaxial, fiber optic, radio wave.
  Protocol – A set of rules that govern data communication. Represent an agreement between the communicating devices.
7

## Slide 8: Example of Protocol
8

## Slide 9: Data representation
Types of data representation
  Text
    In the bit format (“0”,”1”) – bit pattern
    Known as code – a set of bit sequence
    Ie: - Unicode
  Numbers
    Also represented by bit patterns
  Images
    Also represented by bit patterns associated with each pixels.
    Ie: black pixel – all ‘1’s
  Audio
  Video
9

## Slide 10: Transmission mode
Term transmission mode – the direction of signal flow between two linked devices.
There are three types:
  Simplex
  Half-duplex
  Full-duplex
10

## Slide 11: Transmission mode
Simplex
  The communication is unidirectional. Only one of two stations on a link can transmit; the other can only receive
  E.g: keyboards and traditional monitor
Half-Duplex
  Each station can both transmit and receive, but not at the same time.
  When one device is sending, the other can only receive, and vice versa
  The entire capacity of a channel is taken over at the time
  E.g: walkie-talkie
Full-Duplex
  Both stations can transmit and receive simultaneously.
  Like two way street, traffic flowing in both directions at the same time.
  Sharing the capacity of the link.
  E.g: telephone line, videoconferencing
11

## Slide 12: Simplex
12

## Slide 13
Half-Duplex
(Only 1 communication at a single time can be transmitted)
13

## Slide 14: Half-Duplex
14

## Slide 15: Full-Duplex
15

## Slide 16: Networks
A network is a set of devices (often referred to as nodes) connected by communication links (channel).
  A node can be a computer, printer, or any other device capable of sending and/or receiving data generated by other nodes on the network.
Networks use distributed processing, in which task is divided among multiple computers
Network criteria:
  Performance – ie: transmit time and response time
  Reliability – frequency of failure
  Security – protecting data from unauthorized access and damage.
16

## Slide 17: Computer Network and Communication SKR 3200

## Slide 18: Learning outcome
Ilustrate/draw network topology and architecture (C4)
linking the importance of protocols and standards (C3)
Topics
  Topology
  Network models
  Protocol and standard

## Slide 19: Physical Structure
Type of connection
  Point-to-point
  Multipoint
Physical Topology

## Slide 20: Physical Topology
Physical topology – refers to how the network is laid out physically
4 basic topology
  Mesh - dedicated point-to-point link to every other device (see figure 1.5 in the text book)
  Star - dedicated point-to-point link only to a central controller (see figure 1.6 in the text book)
  Bus – all devices are linked through a long cable acts as a backbone (see figure 1.7 in the text book)
  Ring – dedicated point-to-point to its adjacent devices (see figure 1.9 in the text book)
Hybrid topology
  A collection of any two or more basic topology
  Ie: a star backbone + three bus network (fig 1.9)

## Slide 21
A fully connected mesh topology (five devices)
Require a dedicated link
Nodes/Station (n)
> full duplex – n(n-1)/2
5(5-1)/2
= 10 links
Notes: 1.#

## Slide 22
A star topology connecting four stations
Central controller
All communication are through the hub
Is used in Local-Area Network (LAN)
Robustness – when a link fail- only the link is affected
Single point of failure
Less expensive compared to mesh topology
Notes: 1.#

## Slide 23
A bus topology connecting three stations
Connected by drop line and tap
Signal travel through cable = energy are converted to heat
Therefore it become weaker with the distance
Notes: 1.#

## Slide 24
A ring topology connecting six stations
Connected to it immediate neighbours
Add/delete device require two connections
Notes: 1.#

## Slide 25
A hybrid topology: a star backbone with three bus networks
Notes: 1.#

## Slide 26: Categories of Networks
Is based on size, ownership, the distance it covers and physical architecture.
LAN
  Privately owned
  Link the devices in a single office, building, or campus
  Limited to a few kilometer
  Resource sharing between PC/workstation
  Other factor: transmission media and topology
  Most common topologies: bus, ring, star
  Data rate/speed up to 100Mbps
MAN
  Designed to extend over an entire city
  Ex: cable TV network, LAN to LAN resource sharing
  Operates as private company or public company -maxis
26

## Slide 27: Categories of Networks
WAN
  Provides long distance transmission of data, voice, image, video conference over large geographic areas
  May utilize as public, leased or private communication equipment.
  Enterprise network – refer to WAN that wholly owned and used by a single company.

## Slide 28
An isolated LAN connecting 12 computers to a hub in a closet
Notes: 1.#

## Slide 29
WANs: a switched WAN and a point-to-point WAN
Notes: 1.#

## Slide 30
A heterogeneous network made of four WANs and two LANs
Notes: 1.#

## Slide 31: Topology
Hybrid Topologies
Often a network combines several topologies as subnetworks linked together in a larger topology
Several topology can be connected to each other via a central controller in a star topology
31

## Slide 32: WAN Connection (tracert www.fu.is.saga-u.ac.jp)
FSKTM, UPM
IDEC, UPM
JARING MIMOS (MALAYSIA)
TELEGLOBE
(LOS ANGELES, USA)
KYOTO, JAPAN
KYUSHU, JAPAN
SAGA, JAPAN

## Slide 34: Internetworks
Internetwork/internet – two or more networks are connected
Internetworking devices – routers, gateways
internet – a generic term used to mean an interconnection of networks
Internet – a specific worldwide network

## Slide 36
The Internet has revolutionized many aspects of our daily lives. It has affected the way we do business as well as the way we spend our leisure time. The Internet is a communication system that has brought a wealth of information to our fingertips and organized it for our use.
A Brief History
The Internet Today (ISPs)
Topics discussed in this section:
The Internet
Notes: 1.#

## Slide 37
Hierarchical organization of the Internet
Notes: 1.#

## Slide 38
In this section, we define two widely used terms: protocols and standards. First, we define protocol, which is synonymous with rule. Then we discuss standards, which are agreed-upon rules.
Protocols Standards
Standards Organizations Internet Standards
Topics discussed in this section:
Protocols and Standards
Notes: 1.#

## Slide 39
Protocol & Standard
Protocol – set of rules that govern data communication.
  For the simplicity -the protocol is the collection of rules- definition on what, how and when it is communicated.
Key element of a protocol are:
  Syntax – refers to the structure or format of the data, the order in which they are presented.
  Semantics – refers to the meaning of each section bits.
  Timing – refers to two characteristic: when data should be sent, and how fast they can be sent
Standard –provides a model for development that makes it possible for a product to work regardless of individual manufacturer
When no standards, difficulties arise. Example: automobile

## Slide 40: Cont..
Standard – creating and maintaining an open and competitive market for equipment manufacturers, guaranteeing national/international interoperability of data and telecommunications tech process
Data com standard can be categorized to 2:
  De jure (by law/regulation)
    Legislated by an officially recognized body
  De facto (by fact/convention)
    Proprietary, nonproprietary

## Slide 41: Standards Organization
Standard are developed by cooperation among standards creation committees, forums, and government regulatory agencies.
Standards Creation Committees:
  ISO – International Standards Organization
  ITU-T – International Telecommunications Union –Telecommunication Standards Sector
  ANSI – American National Standard Institute
  IEEE- Institute of Electrical and Electronic Engineers
  EIA – Electronic Industries Association
  Telcorda
ISO – multinational body whose membership is drawn mainly from the standards creation committees of various governments throughout the world.
  Aim – to facilitate the international exchange of goods and services by providing models for compatibility

## Slide 42: Standard Organization
ISO – International Standards Organization
This organization contributes to the standardization of large networks, such as Internet standard. ISO developed the OSI model. This model describes the principles of networks, constructing a simple and clear architecture for computer network.
ITU-T – International Telecommunications Union –Telecommunication
ITU is committed to standardizing large telecom networks, such as X.25 and frame relay.
ANSI – American National Standard Institute
This organization defined the standards of FDDI (fiber distributed data interface). It is a voluntary organization.
IEEE- Institute of Electrical and Electronic Engineers
This organization provides standard of network hardware. Based on the standards, hardware manufacturers produce compatible product. IEEE formulated 802. project for LAN including ethernet,token ring,WLAN etc
EIA – Electronic Industries Association
This association defines the standard of network cables, such as cAT5, RS232 etc

## Slide 43: Standards Organization
ITU-T
  formerly known CCITT – Consultative Committee for International Telecommunication Union
  Related to UN which developed standards for telecommunications
  Two popular standards – V series and X series
ANSI
  US non-profit organization
  US representative to both the ISO and the ITU-T
IEEE
  The largest professional engineering society in the world
  Develops standards for computing, communication, electrical engineering and electronics
  Sponsored an important standard for LAN called Project 802

## Slide 44: Standards Organization
EIA
  Association of electronics manufacturers in US
  Responsible for developing the EIA-232-D and EIA-530 standards – define serial transmission between two digital devices. (computer to modem)
Telcordia
  Provides R&D resources for the advancement of telecommunication technology.
  Important source of draft standard to ANSI
Forums
  Telecommunications technology development is moving faster than the ability of standard committee to ratify standards
  Standards committee are procedural bodies and by nature slow moving

## Slide 45: Standards Organization
The forums work with universities and users to test, evaluate and standardize new technologies
At the end, the forums present their conclusion to standards bodies
Example – Frame Relay Forum, ATM Forum, Internet Society (ISOC), Internet Engineering Task Force(IETF)
Regulatory Agencies
  All communication technology is subject to regulation by government agencies such as the Federal Communication Commission (FCC) in US.
Internet Standard
  Tested specification to be used for Internet
  Being published in Internet draft as Request for Comment(RFC) document

## Slide 46: Examples of ISO standard

## Slide 47: IEEE Specification