## Slide 1: COMPUTER NETWORK AND COMMUNICATION CND3200 Topic 2: TCP/IP&Cloud Services
1

## Slide 2: TCP/IP Protocol Suite
Developed prior to the OSI model
5 layers – also known Internet model
The three topmost layers in the OSI model are represented in TCP/IP by a single layer – application layer
TCP/IP is a hierarchical protocol – the upper-level protocol is supported by one or more lower-level protocols
E.g.: @ TL – TCP, UDP; @NL - IP
2

## Slide 3: TCP/IP
Physical layer
  Twisted pair, optical fibers, satellite
Data link layer
  Ethernet, WiFi
Network layer
  IP
Transport layer
  TCP, UDP, SCTP
Application Layer
  SMTP, FTP
3

## Slide 4
1.4
Figure : Communication through an internet (Forouzan, 2013)
To show how the layers in the TCP/IP protocol suite are involved in communication between two hosts
Eg: small internet made up of three LANs (links), each with a link-layer switch. The links are connected by one router
Notes: 1.#

## Slide 5
1.5
Figure : Logical connections between layers in TCP/IP (Forouzan, 2013)
Logical connections
Notes: 1.#

## Slide 6
1.6
Figure : Identical objects in the TCP/IP protocol suite (Forouzan, 2013)
Identical objects (messages)
Identical objects (segment or user datagram)
Identical objects (datagram)
Identical objects (frame)
Identical objects (bits)
Identical objects (datagram)
Identical objects (frame)
Identical objects (bits)
Notes: 1.#

## Slide 7
1.7
Figure : Encapsulation / Decapsulation (Forouzan, 2013)
One of the important concepts in protocol layering in the Internet is encapsulation/ decapsulation.
Notes: 1.#

## Slide 8
Figure 2.16 TCP/IP and OSI model
Notes: 8

## Slide 9
Summary of Layer Functions (TCP/IP)
9

## Slide 10: Example of using TCP/IP
2.10
Addresses in TCP/IP
Prior to the example, you need to know the following terminologies in which will mapped to the TCP/IP model
Notes: 10

## Slide 11
Relationship of layers and addresses in TCP/IP
Notes: 11

## Slide 12: Discussion, Q&A
  Match the following to one or more layers of the OSI Model :
    Route determination
    Connection to transmission media
    Providing services for the end user
    Creating user datagrams
    Transforming bits to electromagnetic signals
    Responsibility for handling frames between adjacent nodes
  What are types of address used in each of the following layers in the TCP/IP protocol?
    Data link layer, network layer, application layer
12

## Slide 13: 2.2 Cloud Services
Cloud definition
Cloud computing is a model for enabling convenient, on-demand network access to a shared pool of configurable computing resources (e.g., networks, servers, storage, applications, and services) that can be rapidly provisioned and released with minimal management effort or service provider interaction (National Institute of Standards and Technology).
This cloud model promotes availability and is composed of five essential characteristics, three service models, and four deployment models.
13
Notes: Lecture notes
*
13

## Slide 14: 2.2 Cloud Services (cont..)
Cloud computing is Internet-based computing, whereby shared resources, software, and information are provided to computers and other devices on demand, like the electricity grid. Cloud computing is a style of computing in which dynamically scalable and often virtualized resources are provided as a service over the Internet. (Wikipedia)
Cloud is a type of parallel and distributed system consisting of a collection of interconnected and virtualized computers that are dynamically provisioned and presented as one or more unified computing resources based on service-level agreements established through negotiation between the service provider and consumers.(Buyya)
14
Notes: Lecture notes
*
14

## Slide 15: 2.2 Cloud Services (cont..)
Analogy - moved to a city and looking for a place to live. Your choice :
Built a new house ? fully control everything your like your new house to have. But that is a hard work …
Buy an empty house ? can customize some part of your house. But never change the original architecture.
Live in a hotel ? Live in a hotel will be a good idea if the only thing you care is enjoy your life!! There is nothing you can do with the house except living in it.

## Slide 16: 2.2 Cloud Services (cont..)
Service Models Overview
Scenario - What if you want to have an IT department ?
Infrastructure as a Service (IaaS) - build a new house?
•You can rent some virtualized infrastructure and build up your own IT system among those resources, which may be fully controlled.
Platform as a Service (PaaS) - buy an empty house?
•You can directly develop your IT system through one cloud platform, and do not care about any lower level resource management.
Software as a Service (SaaS) Similar to live in a hotel?
•You can directly use some existed IT system solutions, which were provided by some cloud application service provider, without knowing any detail technique about how these service was achieved.

## Slide 17: 2.2 Cloud Services (cont..)

## Slide 18: Infrastructure as a Service
Infrastructure as a Service - IaaS
  The capability provided to the consumer is to provision processing, storage, networks, and other fundamental computing resources where the consumer is able to deploy and run arbitrary software, which can include operating systems and applications.
  The consumer does not manage or control the underlying cloud infrastructure but has control over operating systems, storage, deployed applications, and possibly limited control of select networking components .
Examples :
  Amazon EC2
  Eucalyputs
  OpenNebula
  … etc

## Slide 19: Infrastructure as a Service
System architecture :

## Slide 20: Infrastructure as a Service
Enabling technique - Virtualization
  Virtualization is an abstraction of logical resources away from underlying physical resources.
    Virtualization technique shift OS onto hypervisor.
    Multiple OS share the physical hardware and provide different services.
    Improve utilization, availability, security and convenience.
VM1
VM2
VM3

## Slide 21: Infrastructure as a Service
Properties supported by virtualization technique :
  Manageability and Interoperability
  Availability and Reliability
  Scalability and Elasticity

## Slide 22: Infrastructure as a Service
Provide service –Resource Management Interface
  Several types of virtualized resource :
    Virtual Machine – As an IaaS provider, we should be able to provide the basic virtual machine operations, such as creation, suspension, resumption and termination, …etc.
    Virtual Storage – As an IaaS provider, we should be able to provide the basic virtual storage operations, such as space allocation, space release, data writing and data reading, …etc.
    Virtual Network – As an IaaS provider, we should be able to provide the basic virtual network operations, such as IP address allocation, domain name register, connection establishment and bandwidth provision, …etc.

## Slide 23: Infrastructure as a Service
Provide service – System Monitoring Interface
  Several types of monitoring metrics :
    Virtual Machine – As an IaaS provider, we should be able to monitor some system states of each virtual machine, such as CPU loading, memory utilization, IO loading and internal network loading, …etc.
    Virtual Storage – As an IaaS provider, we should be able to monitor some storage states of each virtual storage, such as virtual space utilization, data duplication and storage device access bandwidth, …etc.
    Virtual Network – As an IaaS provider, we should be able to monitor some network states of each virtual network, such as virtual network bandwidth, network connectivity and network load balancing, …etc.

## Slide 24: IaaS - Summary
IaaS is the deployment platform that abstract the infrastructure.
IaaS enabling technique
  Virtualization
    Server Virtualization
    Storage Virtualization
    Network Virtualization
IaaS provided services
  Resource Management Interface
  System Monitoring Interface

## Slide 25: Platform as a Service
Platform as a Service - PaaS
  The capability provided to the consumer is to deploy onto the cloud infrastructure consumer-created or acquired applications created using programming languages and tools supported by the provider.
  The consumer does not manage or control the underlying cloud infrastructure including network, servers, operating systems, or storage, but has control over the deployed applications and possibly application hosting environment configurations.
Examples :
  Microsoft Windows Azure
  Google App Engine
  Hadoop
  … etc

## Slide 26: Platform as a Service
System architecture :

## Slide 27: Platform as a Service
Enabling technique – Runtime Environment Design
  Runtime environment refers to collection of software services available. Usually implemented by a collection of program libraries.
Common properties in Runtime Environment :
  Manageability and Interoperability
  Performance and Optimization
  Availability and Reliability
  Scalability and Elasticity

## Slide 28: Platform as a Service
Provide service – Programming IDE
  Users make use of programming IDE to develop their service among PaaS.
    This IDE should integrate the full functionalities which supported from the underling runtime environment.
    This IDE should also provide some development tools, such as profiler, debugger and testing environment.
  The programming APIs supported from runtime environment may be various between different cloud providers, but there are still some common operating functions.
    Computation, storage and communication resource operation

## Slide 29: Platform as a Service
Provide service – System Control Interface
  Policy-Based Control
    Typically described as a principle or rule to guide decisions and achieve rational outcome(s)
    Make the decision according to some requirements
  Workflow Control
    Describe the flow of installation and configuration of resources
    Workflow processing daemon delivers speedy and efficient construction and management of cloud resources

## Slide 30: PaaS - Summary
PaaS is the development platform that abstract the infrastructure, OS, and middleware to drive developer productivity. PaaS enabling technique
  Runtime Environment PaaS provide services
  Programming IDE
    Programming APIs
    Development tools
  System Control Interface
    Policy based approach
    Workflow based approach

## Slide 31: Software as a Service
Software as a Service - SaaS
  The capability provided to the consumer is to use the provider’s applications running on a cloud infrastructure. The applications are accessible from various client devices through a thin client interface such as a web browser (e.g., web-based email).
  The consumer does not manage or control the underlying cloud infrastructure including network, servers, operating systems, storage, or even individual application capabilities, with the possible exception of limited user-specific application configuration settings.
Examples :
  Google Apps (e.g., Gmail, Google Docs, Google sites, …etc)
  SalesForce.com
  EyeOS
  … etc

## Slide 32: Software as a Service

## Slide 33: Software as a Service
Enabling Technique – Web Service
  Web 2.0 is the trend of using the full potential of the web
    Viewing the Internet as a computing platform
    Running interactive applications through a web browser
    Leveraging interconnectivity and mobility of devices
    Enhanced effectiveness with greater human participation
Properties provided by Internet :
  Accessibility and Portability

## Slide 34: Software as a Service
Provide service – Web-based Applications
  Conventional applications should translate their access interface onto web-based platform.
  Applications in different domains
    General Applications – Applications which are designed for general purpose, such as office suit, multimedia and instant message, …etc.
    Business Applications – Application which are designed for business purpose, such as ERP, CRM and market trading system, …etc.
    Scientific Applications – Application which are designed for scientific purpose, such as aerospace simulation and biochemistry simulation, …etc.
    Government Applications – Applications which are designed for government purpose, such as national medical system and public transportation system service, …etc.

## Slide 35: Software as a Service
Provide service – Web Portal
  Apart from the standard search engine feature, web portals offer other services such as e-mail, news, stock prices, information, databases and entertainment.
  Portals provide a way for enterprises to provide a consistent look and feel with access control and procedures for multiple applications and databases, which otherwise would have been different entities altogether.
  Some examples :
    iGoogle
    MSNBC
    Netvibes
    Yahoo!

## Slide 36: SaaS - Summary
SaaS is the finished applications that you rent and customize.
SaaS enabling technique
  Web Service
SaaS provide services
  Web-based Applications
    General applications
    Business applications
    Scientific applications
    Government applications
  Web Portal

## Slide 37: 2.3 OSI and Cloud Layers

## Slide 38: 2.3 OSI and Cloud Layers (cont..)

## Slide 39: 2.3 OSI and Cloud Layers (cont..)

## Slide 40: 2.3 OSI and Cloud Layers (cont..)

## Slide 41: 2.3 OSI and Cloud Layers (cont..)

## Slide 42: 2.3 OSI and Cloud Layers (cont..)