## Slide 1: Chapter 9 Multiple Core Computers

## Slide 2
Topics
9.1 Multiple core organization
9.2 Graphics Processing Unit (GPU) design
9.3 Usage of GPU as a co-processor

## Slide 3: 9.1 Multiple core organization
A multiple core or multi-core organization is one that combines two or more independent processors into a single package, often a single integrated circuit (IC).
A dual-core device contains two independent microprocessors.
In general, multi-core organization allow a computing device to exhibit some form of thread-level parallelism (TLP) without including multiple microprocessors in separate physical packages.

## Slide 4: Major Technology Providers
The latest versions of many architectures use multi-core, including PA-RISC (PA-8800), IBM POWER (POWER7), SPARC (UltraSPARC IV), and various processors from Intel and AMD.
There is some controversy as to whether multiple cores on a chip is the same thing as multiple processors. Major technology providers are divided on this issue.
IBM considers its dual-core POWER4 and POWER5 to be two processors, just packaged together.
Sun Microsystems, in contrast, considers its UltraSPARC IV to be a multi-threaded rather than multi-processor chip.
Intel considers their multi-core designs to be a single processor.
This is not an idle debate, because software is often more expensive when licensed for more processors.

## Slide 5: Single-core computer

## Slide 6: Multi-core architectures
Replicate multiple processor cores on a single die.
Core 1
Core 2
Core 3
Core 4
Multi-core CPU chip

## Slide 7: Multi-core CPU chip
The cores fit on a single processor socket
Also called CMP (Chip Multi-Processor)
core
1
core
2
core
3
core
4

## Slide 8: The cores run in parallel
core
1
core
2
core
3
core
4
thread 1
thread 2
thread 3
thread 4

## Slide 9: Within each core, threads are time-sliced (just like on a uniprocessor)
core
1
core
2
core
3
core
4
several threads
several threads
several threads
several threads

## Slide 10: Interaction with OS
OS perceives each core as a separate processor
OS scheduler maps threads/processes to different cores
Most major OS support multi-core today

## Slide 11: Why multi-core ?
Difficult to make single-core clock frequencies even higher
Many new applications are
multithreaded
General trend in computer
architecture (shift towards
more parallelism)

## Slide 12: Instruction-level parallelism
Parallelism at the machine-instruction level
The processor can re-order, pipeline instructions, split them into microinstructions, do aggressive branch prediction, etc.
Instruction-level parallelism enabled rapid increases in processor speeds over the last 15 years

## Slide 13: Thread-level parallelism (TLP)
This is parallelism on a more coarser scale
Server can serve each client in a separate thread (Web server, database server)
A computer game can do AI, graphics, and physics in three separate threads
Single-core superscalar processors cannot fully exploit TLP
Multi-core architectures are the next step in processor evolution: explicitly exploiting TLP

## Slide 14: General context: Multiprocessors
Multiprocessor is any computer with several processors
SIMD
  Single instruction, multiple data
  Modern graphics cards
MIMD
  Multiple instructions, multiple data
Lemieux cluster, Pittsburgh supercomputing center

## Slide 15: Multiprocessor memory types
Shared memory: In this model, there is one (large) common shared memory for all processors
Distributed memory: In this model, each processor has its own (small) local memory, and its content is not replicated anywhere else

## Slide 16: Multi-core processor is a special kind of a multiprocessor: All processors are on the same chip
Multi-core processors are MIMD: Different cores execute different threads (Multiple Instructions), operating on different parts of memory (Multiple Data).
Multi-core is a shared memory multiprocessor: All cores share the same memory

## Slide 17: What applications benefit from multi-core?
Database servers
Web servers (Web commerce)
Telecommuncation markets: 6WINDGate (datapath and control plane)
Multimedia applications
Scientific applications, CAD/CAM
In general, applications with Thread-level parallelism (as opposed to instruction-level parallelism)
Each can run on its own core

## Slide 18: More examples
Editing a photo while recording a TV show through a digital video recorder
Downloading software while running an anti-virus program
“Anything that can be threaded today will map efficiently to multi-core”
BUT: some applications difficult to parallelize

## Slide 19
9.2 Graphics Processing Unit (GPU) design
GPU is a graphical processing unit which enables running high definitions graphics on Personal Computers.
Similar to Central Processing Unit (CPU), GPU is a single-chip processor.
The GPU has hundreds of cores as compared to the 4 or 8 in the latest CPUs.
The primary job of the GPU is to compute 3D functions.
GPU parallelism is similar to multicore parallelism

## Slide 20: Parallelism

## Slide 21: Heterogeneous Computing
Host: the CPU and its memory
Device: the GPU and its memory

## Slide 22: GPU vs CPU
A GPU is tailored for highly parallel operation while a CPU executes programs serially
For this reason, GPUs have many parallel execution units and higher transistor counts, while CPUs have few execution units and higher clockspeeds
A GPU is for the most part deterministic in its operation (though this is quickly changing)
GPUs have much deeper pipelines (several thousand stages vs 10-20 for CPUs)
GPUs have significantly faster and more advanced memory interfaces as they need to shift around a lot more data than CPUs

## Slide 23: GPU Architectures
Processing is highly data-parallel
  GPUs are highly multithreaded
  Use thread switching to hide memory latency
    Less reliance on multi-level caches
  Graphics memory is wide and high-bandwidth
Trend toward general purpose GPUs
  Heterogeneous CPU/GPU systems
  CPU for sequential code, GPU for parallel code
Programming languages/APIs
  DirectX, OpenGL
  Compute Unified Device Architecture (CUDA)

## Slide 24: The GPU pipeline
The GPU receives geometry information from the CPU as an input and provides a picture as an output
Let’s see how that happens
host
interface
vertex
processing
triangle
setup
pixel
processing
memory
interface

## Slide 25: Host Interface
The host interface is the communication bridge between the CPU and the GPU
It receives commands from the CPU and also pulls geometry information from system memory
It outputs a stream of vertices in object space with all their associated information (normals, texture coordinates, per vertex color etc)
host
interface
vertex
processing
triangle
setup
pixel
processing
memory
interface

## Slide 26: Vertex Processing
The vertex processing stage receives vertices from the host interface in object space and outputs them in screen space
This may be a simple linear transformation, or a complex operation involving morphing effects
Normals, texcoords etc are also transformed
No new vertices are created in this stage, and no vertices are discarded (input/output has 1:1 mapping)
host
interface
vertex
processing
triangle
setup
pixel
processing
memory
interface

## Slide 27: Triangle setup
In this stage geometry information becomes raster information (screen space geometry is the input, pixels are the output)
Prior to rasterization, triangles that are backfacing or are located outside the viewing frustrum are rejected
Some GPUs also do some hidden surface removal at this stage
host
interface
vertex
processing
triangle
setup
pixel
processing
memory
interface

## Slide 28: Triangle Setup (cont)
A fragment is generated if and only if its center is inside the triangle
Every fragment generated has its attributes computed to be the perspective correct interpolation of the three vertices that make up the triangle
host
interface
vertex
processing
triangle
setup
pixel
processing
memory
interface

## Slide 29: Fragment Processing
Each fragment provided by triangle setup is fed into fragment processing as a set of attributes (position, normal, texcoord etc), which are used to compute the final color for this pixel
The computations taking place here include texture mapping and math operations
Typically the bottleneck in modern applications
host
interface
vertex
processing
triangle
setup
pixel
processing
memory
interface

## Slide 30: Memory Interface
Fragment colors provided by the previous stage are written to the framebuffer
Used to be the biggest bottleneck before fragment processing took over
Before the final write occurs, some fragments are rejected by the zbuffer, stencil and alpha tests
On modern GPUs, z and color are compressed to reduce framebuffer bandwidth (but not size)
host
interface
vertex
processing
triangle
setup
pixel
processing
memory
interface

## Slide 31: Programmability in the GPU
Vertex and fragment processing, and now triangle set-up, are programmable
The programmer can write programs that are executed for every vertex as well as for every fragment
This allows fully customizable geometry and shading effects that go well beyond the generic look and feel of older 3D applications
host
interface
vertex
processing
triangle
setup
pixel
processing
memory
interface

## Slide 32: Diagram of a modern GPU
64bits to
memory
64bits to
memory
64bits to
memory
64bits to
memory
Input from CPU
Host interface
Vertex processing
Triangle setup
Pixel processing
Memory Interface

## Slide 33: CPU/GPU interaction
The CPU and GPU inside the PC work in parallel with each other
There are two “threads” going on, one for the CPU and one for the GPU, which communicate through a command buffer:
CPU writes commands here
GPU reads commands from here
Pending GPU commands

## Slide 34: CPU/GPU interaction (cont)
If this command buffer is drained empty, we are CPU limited and the GPU will spin around waiting for new input. All the GPU power in the universe isn’t going to make your application faster!
If the command buffer fills up, the CPU will spin around waiting for the GPU to consume it, and we are effectively GPU limited

## Slide 35: CPU/GPU interaction (cont)
Another important point to consider is that programs that use the GPU do not follow the traditional sequential execution model
In the CPU program below, the object is not drawn after statement A and before statement B:
Instead, all the API call does, is to add the command to draw the object to the GPU command buffer
Statement A
API call to draw object
Statement B

## Slide 36: Grids, Blocks, and Threads

## Slide 37: CUDA Memory
Fastest, per-thread
Faster, per-block
Slower, global
Read-only, cached

## Slide 38: Graphics Hardware Abstraction
OpenGL and DirectX provide an abstraction of the hardware.

## Slide 39: Programming using CUDA
Compute Unified Device Architecture
do_something_on_host();
kernel<<<nBlk, nTid>>>(args);
cudaDeviceSynchronize();
do_something_else_on_host();
…
Highly parallel

## Slide 40: Example: NVIDIA Tesla
Streaming multiprocessor
8 × Streaming processors

## Slide 41: Example: NVIDIA Tesla
Streaming Processors
  Single-precision FP and integer units
  Each SP is fine-grained multithreaded
Warp: group of 32 threads
  Executed in parallel, SIMD style
    8 SPs × 4 clock cycles
  Hardware contexts for 24 warps
    Registers, PCs, …

## Slide 42: Modern GPU has more ALU’s

## Slide 43
9.3 Usage of GPU as a co-processor
The GPU architecture model. The GPU is a coprocessor to the CPU.
It consists of multiple SIMD multiprocessors, and has a large amount of device memory.
This model is applicable to both NVIDIA's CUDA and AMD's CTM .